## Slide 1
Secure and Robust Ultrasonic sensors for Autonomous Vehicles
Automotive Sensor System SS21
Mayur Tulsibhai Lakhani
(485315)
Technische Universität Chemnitz
Master in Automotive Software Engineering

## Slide 2: Outline
Motivation & Introduction
State-of-the-art of Ultrasonic sensors
Working principle of Ultrasonic Sensor
Different types of attacks & Defense Methodology
PSA functionality, implementation & Experiment results
Conclusion

## Slide 3: Motivation
Automotive Functional Domain
Passenger centric
Auto parking (Body/Comfort)
Vehicle centric [Safety]
Reliability
Should be highly secure
Robust to any type of spoofing & jamming attacks
Lane changing during Autopilot mode (Safety & Cross Domain)
(more critical)
U.S. ultrasonic sensor market size, by type, 2016 - 2027 (USD Million) [8]
Compound Annual
Growth Rate 6 %

## Slide 4: Introduction
The feasibility of Ultrasonic sensor under attacks with moving vehicles[3]
Situation | Decision under Attack | Attacks
W/O obstacles (Create imaginary) | Stop moving | Random spoofing Adaptive spoofing
W/ obstacles (Hide) | Keep moving | Jamming Adaptive spoofing
Ultrasonic sensor’s Operational Frequency(f):
In between 40kHz to 50kHz
f > 50 kHz  attenuation of airborne  Result: weak echoes
f < 40 kHz  interfering sound

## Slide 5: State-of-the-art: Ultrasonic sensors under attacks
 |  | Output under attacks (Spoofing) |  |  | Specifications |  |  | 
Sensor | Freq. | Random | Adaptive | Jamming | Volt. | Measuring Distance | Accuracy | Measuring (Degree)
SRF05 | 40 kHz | Steady | Steady | Min | +5V DC | 2-450cm | 3mm | 15
HC-SRO4 | 40 kHz | Steady | Steady | Min | +5V DC | 2-450cm | 3mm | 15
JSN-SRO4T | 40 kHz | Steady | Steady | Min | +5V DC | 2-450cm | 2mm | 75
US-100 | 40 kHz | Steady | Steady | Min | +5V DC | 2-450cm | 1mm | 30
URM37 | 40 kHz | Steady | Steady | Min | +3.3 -0.5V | 5-500cm | 10mm | 0-180 (Servo)
RCW-0001 | 40 kHz | Steady | Steady | Min | +3 -5.5V | 2-450cm | 10mm | 15
URM04 | 40 kHz | Unsteady | Steady | Min | +5V | 4-500cm | 10mm | 0-180
Grove U. R. | 42 kHz | Steady | Steady | Min | +3.2 -5.2V | 3-350cm | 10mm | 15
SRF01 | 42 kHz | Unsteady | Steady | Min | +3.3-12V | 18-600cm | 10mm | 
MB1200 | 42 kHz | Unsteady | Steady | Max | +3.3-5V | 0-765cm | 10mm | 
Audi Q3 | 50 kHz | Unsteady | Steady | Max |  |  |  | 
Ultrasonic Frequency Range [3]

## Slide 6: Working principle of Ultrasonic sensor
Operational Frequency Range: 30KHz - 180KHz
Where,
TOF: Time of flight
C: Speed of sound waves
D: Distance between sensor and object
Measure the distance by ultrasonic sensor[9]
Emitter
Detector
Obstacle
HC - SR04 Module
Measuring distance from 2cm to 400cm

## Slide 7: Ultrasonic sensors under different types of attacks
Random Spoofing: Replay previously recorded sensor signals to deceive the sensor
Adaptive Spoofing: Creating non existing obstacles
  Step1: receiving sensor signals
  Step2: eliminating echoes
  Step3: transmitting spoof signals
Jamming attacks: Emits high ultrasonic sounds to overwhelm echoes.
[3]

## Slide 8: Defense Enhancement Strategies
Overview of the Defense Scheme Functions[3]
1. PSA | Attacks | Attack Detection |  | Resilient obstacle Detection |  | Attacker Localization | 
Physical Shift Authentication(PSA) Vs. Multiple Sensor Consistency Check (MSCC) | Random Spoofing |  |  |  |  |  | 
 | Adaptive Spoofing |  |  |  |  |  | 
 | Jamming |  |  |  |  |  | 
2.MSCC
1 2
1 2
1 2

## Slide 9: Physical shift Authentication functionality
Customize the ping waveform through randomize certain parameters to corelate the received echo with the ping
Randomize the ping waveform (X). Transmit
Receive, and Measure the echo waveform (Y), where Y = f(X)
if C( x, y ) > α (threshold) , accept the echo else reject, where C is Correlation
Equation of wave form:
t
Where, amplitude, frequency, phase, : ping, : period,

## Slide 10: PSA implementation along with Experiment results
Frequency shift:
shift randomly between different pings
Authentication can be done per ping
y(i ) = x(i)
Amplitude shift:
Received Amp.( ) with Transmitted Amp.
Obstacles  Distances  Attenuation
Amplitude attenuation  linearity  Valid echoes
[3]
[3]
0.212kHz
Detection Range

## Slide 11: PSA implementation along with Experiment results
More than 20 cycles (0.5ms at 40kHz)
Duration of received echoes are approximately liner to those of the corresponding pings.
Y(i) = f(x(i)) = λx(i) + υ; where λ and υ are
constants for a certain obstacle
When the force is shifted to a reverse direction, the membrane gradually decreases the amplitude and then increases following the new phase
[3]
[3]
Duration Shift:
Phase Shift:

## Slide 12: Conclusion
Experiments validate that shifting frequency, amplitude, duration, phase, and period can be used for distinguishing spoofed echoes that does not change in accordance with the modulated pings.
Under the same time efficiency, the performance ranks as:
Frequency Shift > Phase Shift > Amplitude Shift > Duration Shift
Successful detection rate with three cycles of frequency shift is 99.8% and can be increased with wider transducer frequency range
Effective range of the attacks relies on both the operational range of sensors and the transmission power of the attack equipment, which can be improved with budgets.

## Slide 13: References
U. Khalil, A. Nasir, S. M. Khan, T. Javid, S. A. Raza and A. Siddiqui, "Automatic Road Accident Detection Using Ultrasonic Sensor," 2018 IEEE 21st International Multi-Topic Conference (INMIC), Karachi, 2018, pp. 206-212, doi: 10.1109/INMIC.2018.8595541.
B. S. Lim, S. L. Keoh and V. L. L. Thing, "Autonomous vehicle ultrasonic sensor vulnerability and impact assessment," 2018 IEEE 4th World Forum on Internet of Things (WF-IoT), Singapore, 2018, pp. 231-236, doi: 10.1109/WF-IoT.2018.8355132.
W. Xu, C. Yan, W. Jia, X. Ji and J. Liu, "Analyzing and Enhancing the Security of Ultrasonic Sensors for Autonomous Vehicles," in IEEE Internet of Things Journal, vol. 5, no. 6, pp. 5015-5029, Dec. 2018, doi: 10.1109/JIOT.2018.2867917.
Tesla. Model S Software Release Notes V7.1. [Online – Accessed on 14.05.2021]. Available: https://www.tesla.com/sites/default/files/pdfs/release_notes/tesla_model_s_software_7_1.pdf
Tesla. Enhanced Autopilot. [Online - Accessed on 14.05.2021 ]. Available: https://www.tesla.com/de_DE/autopilot
U. Khalil, A. Nasir, S. M. Khan, T. Javid, S. A. Raza and A. Siddiqui, "Automatic Road Accident Detection Using Ultrasonic Sensor," 2018 IEEE 21st International Multi-Topic Conference (INMIC), Karachi, 2018, pp. 206-212, doi: 10.1109/INMIC.2018.8595541.

## Slide 14: References
Marketresearchfuture. “Global Automotive Ultrasonic Sensors Market Research Report”. [Online – Accessed on 28.05.2021]. Available: https://www.marketresearchfuture.com/reports/automotive-ultrasonic-sensors-market-10359
Grandviewresearch. “Ultrasonic Sensors Market Size, Share & Trends Analysis Report By Technology”. [Online – Accessed on 28.05.2021]. Available: https://www.grandviewresearch.com/industry-analysis/ultrasound-sensors-market
Amebaiot. “[RTL8195AM] [RTL8710AF] GPIO - Measure the distance by ultrasonic module”. [Online – Accessed on 14.05.2021]. Available: https://www.amebaiot.com/en/ameba-arduino-gpio-ultrasonic/
Vipul Kushwaha , Sachin Bojewar. “A Survey of Ultrasonic Sensors and their Applications ”, 2019 IJACCE, India, Vol. 8, Issue 11, November 2019, ISSN(Online) 2278-1021. doi: 10.17148/IJARCCE.2019.81120.
Datasheetpdf. “HY-SRF05 Precision Ultrasonic Sensor”. [Online - Accessed on 03.06.2021 ]. Available: https://datasheetspdf.com/pdf-file/813041/ETC/HY-SRF05/1
Dfrobot. “URM37 Ultrasonic Sensor (2～800cm)”. [Online - Accessed on 03.06.2021 ]. Available: https://www.dfrobot.com/product-53.html
Cytron. ”RCW-001 Micro Ultrasonic Range”. [Online - Accessed on 03.06.2021 ] . Available: https://www.cytron.io/p-rcw-0001-micro-ultrasonic-range

## Slide 15: References
Dfrobot. “URM04 Ultrasonic Sensor”. [Online - Accessed on 03.06.2021 ] . Available: https://www.dfrobot.com/product-101.html
Cdn-reichelt. “Grove - Ultrasonic Ranger ”. [Online - Accessed on 03.06.2021 ] . Available: https://cdn-reichelt.de/documents/datenblatt/A300/101020010_01.pdf

## Slide 16
Thank You!

## Slide 17: HC SR04 - Test Cases [2]
1. Thine Object as an obstacle (r=30cm)
2. Covering Transmitter & Reciver( cardboard)
3. Acoustic Foam (r =35cm extended)
4. Interference with Additional Sensors